## Slide 1: Introduction to MIMOSA’s Open System Architecture For Enterprise Application Integration (OSA-EAI) July 2003
Ken Bever
MIMOSA Technical Director
ISO TC108/SC5/WG6 Convenor
ANSI S2/WG10/Panel 5 Convenor
President & Principal Consultant, SolutionTech
kbever@mimosa.org

## Slide 2
Gateway
Gateway
Gateway
Gateway
Gateway
Gateway
Control Systems,
Plant Historians,
& Production
Schedulers
Enterprise
Resource Planning
(ERP) Systems
Engineering
Product Data
Mgmt. Systems
Condition Monitoring
Systems
Maintenance
Scheduling & MRO
Inventory (EAM/
CMMS) Systems
Remote Analysis/
Diagnostic/Prognostic
& Reliability Systems
Problem Today In Equipment Asset Management: Islands of Information

## Slide 3
Problem Today In Equipment Asset Management: Islands of Information

## Slide 4: Problem Today In Equipment Asset Management: Islands of Information
“Information islands” -- specialized, proprietary systems, optimized for a specific task or tasks, provide best results and value
Each island speaks a different data “language”
Warning!
Que?
†Èµ
Notes: 31
14

## Slide 5: Integration Option #1: Avoid Bridge-Building
Purchase as many systems as possible from one vendor
  Advantages:
    Single-source to resolve problems / incompatibilities
    Low risk
  Disadvantages
    Not possible to get a complete off-the-shelf solution from one supplier
    Possibly dependent on proprietary interfaces
    Each product may not be the “best-of-breed” solution
    Less customization

## Slide 6: Integration Option #2: Buy a Custom Bridge
Buy a Pre-designed Gateway Offered By A Supplier
  Advantages:
    Lower cost: Cost shared among all who purchase the gateway
    Lower risk than using internal IS resources to build a gateway
  Disadvantages
    Possibly dependent on proprietary interfaces
    If relationship between the two suppliers sours, then gateway is in jeopardy
    Must continually buy/fund updates to the gateway for new system versions
    Less customization

## Slide 7: Integration Option #3: Build a Custom Bridge
Build Your Own Gateway Through Integration Company or Internal IT Group
  Advantages:
    Highly customizable to plant needs
    Short-term strategic benefit to company
  Disadvantages
    High risk due to unforeseen incompatibility issues
    High cost due to lack of multiple users
    Difficult to resolve problems -- finger-pointing possible with suppliers
    Possibly dependent on proprietary interfaces
    High annual software maintenance cost (estimated 20% of original cost)
      $1 Million Integration Project ($200,000 annual maintenance cost)

## Slide 8: Integration Option #4: Use an Open System Bridge
Build or Buy an Industry-Standard Gateway
  Advantages:
    Engineered Plug-and-Play System Capability Designed Up-front Into System
    Saves You From Burden of On-going Integration Efforts
    More Freedom to Choose Best Technology From Information Supplier (Plug & Play)
    Forms the Information Backbone of e-Maintenance
  Disadvantages
    Suppliers Must Support Industry Standard
    Standard Gateway May Have Some Performance Degradations from Custom Interface

## Slide 9: Definition of a Universal, Open Interface
An Interface Where Software Components Are Able to Automatically Communicate Without Any Proprietary or Supplier-Specific Interface Protocols
  Zip Compression Format
  PCMCIA Card
  RTF Report Format
  OPC Process Control Interface
  MIMOSA Maintenance/Reliability Open Interfaces

## Slide 10: Why is the Open Systems Approach Preferable?
End-user Perspective
  Plug-and-Play System Capability Designed Up-front Into System
  Saves End-User Burden of On-going Integration Efforts
  More Freedom to Choose Best Technology From Information Supplier (Plug & Play)
Supplier Perspective
  Concentrate Resources on Highest Value, Core Competency Instead of Low Value Platform and Custom Interface Requirements
  Stimulate New Markets & Expansion of Industry
Notes: 36

## Slide 11
Gateway
Gateway
Gateway
Gateway
Gateway
Gateway
Control Systems,
Plant Historians,
& Production
Schedulers
Enterprise
Resource Planning
(ERP) Systems
Engineering
Product Data
Mgmt. Systems
Condition Monitoring
Systems
Maintenance
Scheduling & MRO
Inventory (EAM/
CMMS) Systems
Remote Analysis/
Diagnostic/Prognostic
& Reliability Systems
Problem Today In Equipment Asset Management: What’s the Solution to the Islands of Information?

## Slide 12
Gateway
Gateway
Gateway
Gateway
Gateway
Gateway
Control Systems,
Plant Historians,
& Production
Schedulers
Enterprise
Resource Planning
(ERP) Systems
Engineering
Product Data
Mgmt. Systems
Condition Monitoring
Systems
Maintenance
Scheduling & MRO
Inventory (EAM/
CMMS) Systems
Remote Analysis/
Diagnostic/Prognostic
& Reliability Systems
The Solution To Equipment Asset Management: Utilize Open System Gateways
Open Operations and Maintenance Information Bus

## Slide 13
MIMOSA OSA-EAI
MIMOSA OSA-EAI
MIMOSA OSA-EAI
Condition Monitoring
Systems
Maintenance
Scheduling & MRO
Inventory (EAM/
CMMS) Systems
Remote Analysis/
Diagnostic/Prognostic
& Reliability Systems
The Solution To Equipment Asset Management : Utilize Open System Gateways
Open Operations and Maintenance Information Bus

## Slide 14: What Is The Machinery Information Management Open Systems Alliance (MIMOSA)?
A not-for-proft trade organization dedicated to developing and encouraging adoption of open information standards for Operations and Maintenance
50+ Sponsors & Members in 9 Countries
  Solution Technology Vendors
    Condition Monitoring / Condition-based Maintenance (CBM) Solution Vendors
    Computerized Maintenance Management System (CMMS)/Enterprise Asset Management (EAM) Vendors - (Maintenance Logistics System Vendors)
  Capital Equipment OEMs
  Systems Integrators
  Equipment Operators & Maintainers
  MRO Solutions Consultants

## Slide 15: MIMOSA Sponsors

## Slide 16: The Vision of MIMOSA
Open MRO Information System Integration Enables:
  Multi-Vendor Solutions
  Cross Platform Solutions
  Cross Industry Solutions
  Comprehensive Maintenance & Repair Solutions Properly Incorporating Corrective Maintenance (CM), Preventive Maintenance (PM) & Condition Based Maintenance (CBM)
  Standardized Asset Registry Information Facilitates:
    Integration with EAM/CMMS, Reliability Systems, & Condition Monitoring Systems for Complete MRO Solutions
    Service-Segments and Assets can be tracked over their life-cycles for Asset Management Requirements
  Standardized Maintenance Work Request Creation/Tracking Facilitates:
    Integration with EAM / CMMS Systems
    Work Requests / Standardized Work “Solution” Packages Can Be Invoked
    Actual Work Completed Can Be Queried

## Slide 17: The Value of MIMOSA
Specifications - Open, Industry-Built, Robust Condition-based Maintenance (CBM) and MRP Enterprise Application Integration (EAI) Specifications
  Enabling end-to-end, vertical & horizontal information integration
  XML-based specifications are true enabler for multi-vendor e-maintenance initiatives
  Faster, better & cheaper solutions
Trade Association – Cooperative MRO Market Development
Value Added Network – MIMOSA Information Network™ (MIN)
MRO Industry Forum – Subject Matter Experts in the Cross Disciplinary Technologies, Products & Services needed to enable Complex MRO Solutions for:
  Heavy Equipment OEM’s
  Equipment operators & maintainers
  CBM vendors & subject matter experts
  EAM/CMMS vendors & subject matter experts
  IS/IT subject matter experts
Advocacy- MRO Industry-Sponsored Advocate for:
  The capture, use & reuse of consistently defined MRO information
  Open, industry-driven collaboration on the needed solutions

## Slide 18: Government-Related MIMOSA MRO Initiatives
Partnership with the OSA-CBM Program
Strategic Relationship with Army PM-TMDE
  At Platform Commitment
  Fleet Management Project
Project with Army CECOM/TMDE/TACOM/CASCOM
  Telemaintenance Architecture Development
  Concept Prototype & Demonstration Project
NAVSEA-TOSA Program
  MIMOSA Member
  Joint Services Demonstration Project
National Institute of Building Sciences (NIBS)
  Reciprocal Memberships
  Facilities Management Standard Development
  Joint Demonstration Project Under Discussion

## Slide 19
Asset Optimization
&
Decision Support Systems
Maintenance Management Systems
Enterprise Asset Maintenance Systems
Call Center / Logistics Management
Operator Human-Machine Interfaces
Production Scheduling Systems
Manufacturing Execution Systems
Open Operations
Open Maintenance
OpenO&MTM Information Standards
Control / On-line Monitoring Systems
Operational Data Historian Systems
Periodic Monitoring Systems
Open Asset
Management
OPC XML-DA / XML A&E
Operational Real-time Data & Alarms
OSA-EAI
Operational Archived Data & Alarms
MIMOSA OSA-EAI
Complex Real-time Data & Alarms
MIMOSA OSA-EAI
Complex Archived Data & Alarms
MIMOSA
OSA-EAI
Maint. Action Request
MIMOSAOSA-EAI
OPC
XML-DA
Complex
Operator Action Request with Findings
Notes: Scenario #1
Decision Support System (DSS) is notified by the Operational Data Historian System (ODHS) that a fluid-handling process containing a turbine-driven boiler feed pump is slowing degrading, though not enough to trigger an OP-actionable alarm.
Scenario #2
The DSS queries additional data about the turbine pump from the On-line Condition Monitoring System (OCMS), which sends turbine shaft displacement data.
Scenario #3
The DSS queries additional data about the pump from the Periodic Monitoring Systems, which are a portable casing vibration monitoring system and an oil sampling data….. The DSS determines in advance that the turbine’s thrust bearing is heading for trouble and internally generates a health assessment, diagnosis with explanation, and prognosis.
Scenario #4
The DSS next automatically issues a maintenance action request to the Enterprise Asset Maintenance (EAM) work queue with a recommended maintenance action (REPLACE TURBINE THRUST BEARING BY <date>), appropriate solution package (pre-planned work template), and health assessment diagnosis and prognosis.
Scenario #5
Before operator (OP) would normally be given an alarm – DSS issues an operator action request to the HMI. This contains a recommended operator action (i.e. SLOW DOWN PROCESS to 80%), and notifies OP that a recommended maintenance action has been placed in an EAM work queue and provides OP with the work request lookup identifier.
Scenario #6
OP is watching the Human-Machine Interface (HMI) and notices a predictive operations action request in the queue. OP reviews the request and wants to confirm the findings of the DSS. Using the HMI, OP reviews current operational data and turbine condition health reports from the DSS (PDF format), and verifies the findings. OP changes process speed to 80%.
Scenario #7
OP launches the EAM and approves the maintenance action inside the EAM system using the work request tracking number provided earlier.

## Slide 20: MIMOSA OSA-EAI Architecture Summary
Supplier-built
Production
Beta
Draft
Design Phase
Categories [Category]
Service Segments (“As Designed” Functional Blocks)
Asset (“As Installed” Serialized Physical Objects)
Tech-File
Import
V 2.2
Software
Tech-File
Export
V2.2
Software
Tech-Web
Client
V2.2
Software
Tech-Web
Server
V2.2
Software
Tech-SQL
Client
for Category
V 1.1 Soft.
Tech-SQL
Server
for Category
V 1.1 Soft.
Tech-File
Import
for Category
V 1.1 Soft.
Tech-File
Export
for Category
V 1.1 Soft.
Tech-SQL
Client
for Category
V 1.1 Spec.
Tech-SQL
Server
for Category
V 1.1 Spec.
Tech-File
Import
for Category
V 1.1 Spec.
Tech-File
Export
for Category
V 1.1 Spec.
Tech-File
Import
V2.2
Spec. [XSD]
Tech-File
Export
V2.2
Spec. [XSD]
Tech-Web
Client
V2.2
Spec. [XSD]
Tech-Web
Server
V2.2
Spec. [XSD]
ODBC SQL/CLI
Specification
MIMOSA Export
Data (MED) File
Specification
Common Relational Information
Schema V1.1 Specification
MIMOSA Site0 Reference DB
V1.1 [MED]
CRIS Site0 Reference DB
V2.2 [XML]
Common Relational Information Schema (CRIS) V2.2 Specification [XSD]
Tech-OPC
Client
V2.2
Spec.
OSA-EAI Terminology Dictionary [PDF] & OSA-EAI Common Conceptual Object Model (CCOM) [UML] V0.2
Tech-XML
Client/Server Schema V2.2 [XSD]
Packaged Technologies [Tech-]
REG (Asset Register Management)
WORK (Work Management)
DIAG (Diagnostics / Health / Rec.) TREND (Static Trends/Alarms)
DYN (Dynamic Vibration/Sound)
SAMPLE (Oil/Fluid/Gas/Solid Tests)
BLOB (Binary Data/Thermography)
REL (Reliability / Data)
Revised April 30, 2003
Tech-OPC
Server
V2.2
Spec.
Tech-XDE
Client
V2.2
Spec.
Tech-XDE
Server
V2.2
Spec.
Tech-OPC
Client
V2.2
Spec.
Tech-OPC
Server
V2.2
Spec.
Tech-XDE
Client
V2.2
Spec.
Tech-XDE
Server
V2.2
Spec.

## Slide 21: MIMOSA OSA-EAI Interfaces
MIMOSA OSA-EAI Core Technology
  Built upon a Common Relational Information Schema (CRIS)
  Specifications packaged for Interoperability of:
    Asset Registries
    Work Management Systems
    Diagnostic / Health Assessment Systems
    Process Data Historian Systems
    Dynamic Vibration / Sound Data Historian Systems
    Sample Test Data Historian Systems
    Binary / Thermography Data Historian Systems
    Reliability Database Systems
  Designed to Transfer Archived Data Which Is Normally Stored in a Database
  No Middleware Required
  Tech-XML Schema defines the information content for Client/Server interfaces which querying and/or create CRIS information
Notes: At MIMOSA’s second meeting, we formed 2 sub-committees. One was concerned with plug-and-play Data Exchange Standards and the other with plug-and-play Programmatic Interface Standards. Both sub-committees surveyed the available open technology coming from the computer industry.
Committee #1 (Data Exchange Standards) thought it possible to develop a common relational schema and then create standard ASCII files of data conforming to the standard and standard ODBC SQL queries from a data source which conformed to the standard. From this Committee, came the MIMOSA Type I interfaces based upon MIMOSA’s Common Relational Information Schema (CRIS). These Type I interfaces would be designed to transfer archived data/information which would normally be stored in a database or memory buffer between 2 different computer platforms. All production specifications developed to-date are Type I interfaces.

## Slide 22: MIMOSA-Defined Interfaces
MIMOSA OSA-EAI Interfaces
  Tech-File Interfaces define bulk XML file import/exports for any transport protocol
  Tech-Web Interfaces define HTTP Post Client/Server interfaces based on Tech-XML schema
  Tech-OPC Interfaces define OPC XML-DA Complex Standard Client/Server interfaces using Tech-XML schema(under development)
  Tech-XDE (XML Document Exchange) Interfaces allow user-defined Tech-XML Schema to be exchanged using a user-defined transport mechanism
Notes: At MIMOSA’s second meeting, we formed 2 sub-committees. One was concerned with plug-and-play Data Exchange Standards and the other with plug-and-play Programmatic Interface Standards. Both sub-committees surveyed the available open technology coming from the computer industry.
Committee #1 (Data Exchange Standards) thought it possible to develop a common relational schema and then create standard ASCII files of data conforming to the standard and standard ODBC SQL queries from a data source which conformed to the standard. From this Committee, came the MIMOSA Type I interfaces based upon MIMOSA’s Common Relational Information Schema (CRIS). These Type I interfaces would be designed to transfer archived data/information which would normally be stored in a database or memory buffer between 2 different computer platforms. All production specifications developed to-date are Type I interfaces.

## Slide 23: OSA-EAI Common Conceptual Object Model (CCOM) & Common Relational Information Schema (CRIS)
  Site Identification
    Normally D-U-N-S business location identifier
  Asset Identification
    Universal asset “birth” tag
    Allows birth to death asset tracking
    Nameplate and “anatomy” specification data
  Service Segment Identification
    Universal functional location tag
    Allows tracking of where an asset was in use over time
  Condition/Operating Measurement Location
    Universal measurement location tag
    Facilitates integration of multiple monitoring technologies
  Current/Historical Measurement Data
    Dynamic (Vibration/Sound) FFT, Time-waveforms
    Scalar (Process)
    BLOB (Documents / Image / Thermographic)
    Sampling (Fluid / Air / Gas)
  Diagnostic/Health/Prognostic Information
  Advisory Recommendation Information
  Maintenance Work Requests / Work Schedules / Work Histories
  Production Requests / Production Schedules / Production Histories
  Reliability/FMECA/Root Cause Data
Notes: MIMOSA’s experts from across the globe have spent over 5 years in developing a common information schema which allows information from many systems to be communicated and integrated. The schema is in a relationship form and so is known as CRIS -- Common Relational Information Schema.
It contains standard site, asset, and functional service segment idenficiation nomenclature. In addition, it provides for a method of standard measurement location identification across various condition monitoring technologies (dynamic, scalar, binary [BLOB], and sampling). CRIS also allows the communication of diagnostic, health, and prognostic information from smart systems and eases the generation of advisory recommendations. CRIS models maintenance and production work request scheduling and tracking the actual completion of a maintenance or production job as related to an asset. CRIS also provides the information framework for storing reliability data for assets.

## Slide 24
Models
Sites
Segments
Assets
Utilization
Measurement Locations
Databases
Reference Tables
Ordered Lists
MIMOSA Reference
Database Entries
OSA-EAI Common Conceptual Object Model (CCOM) & Common Relational Information Schema (CRIS)
Networks / Processes
Functions
Hypothetical / Proposed Events
Solution Packages
Work Requests / Work Orders
Events / Alarms
Measurement Events
Scalar Data & Alarms
Dynamic Data &Alarms
BLOB Data & Alarms
Sample Data & Alarms

## Slide 25: OSA-EAI Basic Principles
In order to guarantee “plug-and-play” interoperable OSA-EAI systems, users and suppliers of MIMOSA systems must agree to abide by certain conventions regarding the assignment of globally-unique ID’s (GUID’s). A “registration authority” for certain key CRIS tables must manages a pool of unique GUID’s.
Registration Authorities are:
  EAI Level: MIMOSA / Dunn & Bradstreet
    Site Level: End-User
      Database Level: System Application
Notes: MIMOSA’s experts from across the globe have spent over 5 years in developing a common information schema which allows information from many systems to be communicated and integrated. The schema is in a relationship form and so is known as CRIS -- Common Relational Information Schema.
It contains standard site, asset, and functional service segment idenficiation nomenclature. In addition, it provides for a method of standard measurement location identification across various condition monitoring technologies (dynamic, scalar, binary [BLOB], and sampling). CRIS also allows the communication of diagnostic, health, and prognostic information from smart systems and eases the generation of advisory recommendations. CRIS models maintenance and production work request scheduling and tracking the actual completion of a maintenance or production job as related to an asset. CRIS also provides the information framework for storing reliability data for assets.

## Slide 26: MIMOSA/Dunn & Bradstreet Maintained EAI-Level GUID’s
Site GUIDs (Site.site_id:int)
  For industrial facility and plant locations, use Dunn & Bradstreet-assigned D-U-N-S integer
  For governmental, non-profit, and other sites without a D-U-N-S number, MIMOSA will assign a range of numbers to a corporate entity. This corporate entity will then assign unique site_id’s to their various locations.
  For fleet applications, this entity represents a “mobile platform”, which could be an aircraft carrier, a jet, or an automobile. Due to the quantity of mobile platforms and the need for each to be their own registration authority, an expanded site GUID is planned for CRIS V3. Until then, fleet applications should use the single integer as a site GUID.
Notes: MIMOSA’s experts from across the globe have spent over 5 years in developing a common information schema which allows information from many systems to be communicated and integrated. The schema is in a relationship form and so is known as CRIS -- Common Relational Information Schema.
It contains standard site, asset, and functional service segment idenficiation nomenclature. In addition, it provides for a method of standard measurement location identification across various condition monitoring technologies (dynamic, scalar, binary [BLOB], and sampling). CRIS also allows the communication of diagnostic, health, and prognostic information from smart systems and eases the generation of advisory recommendations. CRIS models maintenance and production work request scheduling and tracking the actual completion of a maintenance or production job as related to an asset. CRIS also provides the information framework for storing reliability data for assets.

## Slide 27: End-User Maintained Site-Level GUID’s
Database GUIDs (Site_Database.db_id:int)
  The end-user at a site must assign a unique, non-changeable integer to every MIMOSA-compliant database at a site.
Segment GUIDs (Segment.segment_id:int)
  A segment is a functional decomposition of a site where physical assets can be installed or assigned. The end-user at a site must allocate a pool of valid segment identifier integers to applications which must “birth” segments.
Asset GUIDs (Asset.asset_id:int)
  An asset is a physical instance of a piece of equipment. The end-user at a site must allocate a pool of valid asset identifier integers to applications which “birth” assets. Once “”born”, the asset’s GUID should never change, even if it is moved to another site or sold to another end-user.
Measurement Location GUIDs (Meas_Location.meas_loc_id:int)
  The end-user at a site must allocate a pool of measurement location GUIDs to applications which monitor various aspects of segments/assets and need to “birth” measurement locations.
Agent GUIDs (Site_Database.db_id:int)
  An agent is an intelligent person, group, or system. The end-user at a site must allocate a pool of valid agent identifier integers to application which “birth” agents. Once “born”, the agent’s GUID should never change, even though the agent moves to another site.
Notes: MIMOSA’s experts from across the globe have spent over 5 years in developing a common information schema which allows information from many systems to be communicated and integrated. The schema is in a relationship form and so is known as CRIS -- Common Relational Information Schema.
It contains standard site, asset, and functional service segment idenficiation nomenclature. In addition, it provides for a method of standard measurement location identification across various condition monitoring technologies (dynamic, scalar, binary [BLOB], and sampling). CRIS also allows the communication of diagnostic, health, and prognostic information from smart systems and eases the generation of advisory recommendations. CRIS models maintenance and production work request scheduling and tracking the actual completion of a maintenance or production job as related to an asset. CRIS also provides the information framework for storing reliability data for assets.

## Slide 28: System Application Maintained Database-Level GUID’s
Reference “Type” and Manufacturer GUIDs
  For non-MIMOSA entries, the application will need to assign unique local identifiers.
Ordered List GUIDs (Ordered_List.ord_list_id:int)
Network/Process GUIDs (Network.network_id:int)
Segment Type/Asset Type/Model/Segment/Asset Hypothetical Event GUIDs (Table.tababbrev_hyp_event_id:int)
Segment Type/Asset Type/Model/Segment/Asset Proposed Event GUIDs (Table.tababbrev_prop_event_id:int)
Solution Packages (Solution_Package.sol_pack_id:int)
Work Requests (Work_Request.work_req_id:int)
Work Order (Work_Order.work_order_id:int)
Notes: MIMOSA’s experts from across the globe have spent over 5 years in developing a common information schema which allows information from many systems to be communicated and integrated. The schema is in a relationship form and so is known as CRIS -- Common Relational Information Schema.
It contains standard site, asset, and functional service segment idenficiation nomenclature. In addition, it provides for a method of standard measurement location identification across various condition monitoring technologies (dynamic, scalar, binary [BLOB], and sampling). CRIS also allows the communication of diagnostic, health, and prognostic information from smart systems and eases the generation of advisory recommendations. CRIS models maintenance and production work request scheduling and tracking the actual completion of a maintenance or production job as related to an asset. CRIS also provides the information framework for storing reliability data for assets.

## Slide 29
MIMOSA Common Relational Information Schema (CRIS)
MIMOSA OSA-EAI Architecture
Vendor A Supplied
Vendor B Supplied
MIMOSA Supplied
Vendor A
Database
Vendor B
Database

## Slide 30: MIMOSA’s Reference Database: Site Zero
Asset Type Codes
  Universal asset type taxonomy
  Allows standard querying of common asset types, I.e., “Centrifugal Pump”
Service Segment Codes
  Universal service segment type taxonomy
  Allows standard querying of segment type, I.e, “Boiler Feed Pump”
  Allows tracking of where an asset was in use over time
Condition/Operating Measurement Location Codes
  Universal measurement location tag
  Facilitates integration of multiple monitoring technologies
Measurement Parameter Data Codes
  Dynamic (Vibration/Sound) FFT, Time-waveforms Parameter Codes
  GMT/UTC Timestamping with Local Time Offset
  Standard Engineering Units Related to SI Reference Units
  Quality Codes
  Sampling Test Codes
Diagnostic/Health/Prognostic Event Codes
Failure/Root Cause Codes
Notes: In addition to CRIS, MIMOSA experts have generated a large reference database, called the MIMOSA Site Zero Reference Database. This contains many useful codes which allow standardization across many disparate systems -- even those from various countries. For example, the Site Zero database contains a standard universal asset type taxonomy, which allows standard querying of common asset types such as “Centrifugal Pump” which has never-changing 3-integer unique identifier. Other standard code tables include: service segment, measurement location, engineering units, sampling test codes, diagnostic/prognostic event codes, health codes, failure codes, and root cause codes.

## Slide 31
MIMOSA Common Relational Information Schema (CRIS) Version n.n
MIMOSA Site0 Reference DB Version n.n-yyyy.mm.dd
MIMOSA OSA-EAI Architecture
Vendor A Supplied
Vendor B Supplied
MIMOSA Supplied
Vendor A
Database
Vendor B
Database

## Slide 32
Notes: Here is an example of codes from Asset Type table of MIMOSA’s Site Zero reference database. You will see that a “Journal Bearing” has a code of 0-0-367.

## Slide 33
MIMOSA Tech-FILE Export for
Category Version n.n Specification
Common Relational Information Schema (CRIS) Specification
MIMOSA Export Data (MED) File Specification
MIMOSA Tech-File Architecture
Technologies
TREND (Trends/Alarms)
DYN (Dynamic Vibration/Sound)
Vendor A
Database
Vendor B
Database
Tech-FILE Import for
Category Version n.n Specification
Vendor A MIMOSA Tech-File for
Category Version n.n Export Software
Vendor B MIMOSA Tech-File for
Category Version n.n Import Software
MED Files
Categories
Service Segments (Functional Locations)
Vendor A Supplied
Vendor B Supplied
MIMOSA Production
MIMOSA Beta
MIMOSA Site0 Reference DB Version n.n-yyyy.mm.dd
Notes: Condition monitoring systems have a choice of three MIMOSA technologies to communicate their data to the PAM system. The first, and oldest technology is the Tech-File Export Server which creates standard export data files, called MIMOSA Export Data (MED) files. There are four applicable data-level specifications:
Dyn-File Export & Import (for dynamic vibration & sound measurements)
Trend-File Export & Import (for process & scalar measurements)

## Slide 34
MIMOSA Tech-SQL Server for
Category Version n.n Specification
MIMOSA Common Relational Information Schema (CRIS)
MIMOSA SQL/Call Level Interface Specification
MIMOSA Tech-SQL Architecture
Vendor A
Database
Vendor B
Database
MIMOSA Tech-SQL Client for
Category Version n.n Specification
Vendor A MIMOSA Tech-SQL for
Category Version n.n Server Software
Vendor B MIMOSA Tech-SQL for
Category Version n.n Client Software
CRIS SQL Query
CRIS Data Set
Vendor A Supplied
Vendor B Supplied
MIMOSA Production
MIMOSA Beta
Technologies
TREND (Trends/Alarms)
DYN (Dynamic Vibration/Sound)
Categories
Service Segments (Functional Locations)
MIMOSA Site0 Reference DB Version n.n-yyyy.mm.dd

## Slide 35: XML
eXtensible Markup Language (actually a “metalanguage”)
Developed by the World Wide Web Consortium (W3C) beginning in 1996
Became a W3C standard in February 1998
Universal format for structured documents and data on the web

## Slide 36: XML
Lets different systems exchange data
Lets you sort, select, and manipulate the data in documents, on the server, or on the client machine
Includes XSL – eXtensible Style Language (follow on to CSS)

## Slide 37
Industry Activity With XML
W3C
XML.org/OASIS
BizTalk.org
Rosettanet
OAGI
MIMOSA
CommerceOne
Ariba
FINXML
HL7
XML/EDI
CommerceNet
Defining XML
Defining Content
XML Respositories
Promoting eCommerce

## Slide 38: MIMOSA OSA-EAI V2.2 Interface Concepts
General – All MIMOSA OSA-EAI Interfaces are based on MIMOSA’s Common Relational Information Schema (CRIS). While prior versions of MIMOSA Interfaces have used a variety of enabling technologies, all OSA-EAI V2.2 interfaces will use XML Schema as defined by the W3C.
Tech-XML V2.2 Client/Server Schema – This schema enables is based on a client/server model and has been logically organized into Schema Sets or Applications Program Interfaces (APIs) designed to support a series of MIMOSA Application Technology Types.
Tech-File V2.2 Interface – These interfaces are designed to enable the direct transfer of one entire persistent data store to another one in an industry- standard XML format. They are similar in concept to the earlier Tech-File interfaces, but rather than importing/exporting individual files in a comma delimited format, they enable the transfer of packaged XML documents containing all of the available data. Any given application may include import and/or export capability based on these MIMOSA specifications.
Tech-Web V2.2 Interfaces – These Web-enabled (HTTP) interfaces implement onTech-XML schema to enable the integration of loosely-coupled applications into an Open MRO solution in an industry-standard fashion.).

## Slide 39: MIMOSA Tech-Web V2.2 Interfaces
REG-Web (Asset Register Management) – Enables the integration of Open MRO Applications needing to exchange asset catalog registry information in an industry standard format. The registry includes both asset-specific nameplate information and segment related information. Segment information provides the functional relationship to other segments in a process model while asset information provides the data for the current instance of any asset installed in a given segment. This approach enables life-cycle tracking of MRO data by segment or asset.
WORK-Web (Work Management) – Enables the integration of Open MRO Applications needing to exchange information about request for work and work request along with associated work orders and solution packages that are related to serialized assets or service segments.
DIAG-Web (Diagnostics / Health / Rec.) - Enables retrieval of human or "smart-agent" generated current and/or future proposed asset health states, current and/or future proposed diagnostic failure modes and casual trees, remaining useful life predictions, and recommendations. Also allows access to measurement evidence supporting the diagnoses/prognoses.
  For: Diagnostic Systems
  Prognostic Systems
TREND-Web (Static Trends/Alarms) - Enables retrieval of historical scalar measurements, abnormal data alarms, and operational event logs
  For: Process Data Historians
  Process Condition Monitoring Systems
  Operational Data Systems
DYN-Web (Dynamic Vibration/Sound) - Enables retrieval of historical dynamic measurements (used with vibration and sound monitoring and including frequency spectra measurements and time waveforms), abnormal data alarms, and operational event logs
  For: Vibration Condition Monitoring Systems
  Sound Condition Monitoring Systems

## Slide 40: MIMOSA Tech-Web V2.2 Interfaces (Cont.)
SAMPLE-Web (Oil/Fluid/Gas/Solid Tests) - Enables retrieval of historical fluid, air, and solid sampling data, abnormal data alarms, and operational event logs
  For: Oil Sampling Condition Monitoring Systems
  Air Sampling Condition Monitoring Systems
  Solid Sampling Condition Monitoring Systems
BLOB-Web (Binary Data/Thermography) - Enables retrieval of historical binary large objects (BLOB) measurements (used with thermography and imaging monitoring), abnormal data alarms, and operational event logs
  For: Thermographic Condition Monitoring Systems
  Image Monitoring Systems
REL-Web (Reliability Data) – Enables retrieval of FMECA & RCM analyses and historical failure histories

## Slide 41
Tech-Web Server
Version n.n Specification
MIMOSA Common Relational Information Schema (CRIS)
Tech-XML Client/Server Schema V2.2
MIMOSA Tech-Web Architecture
Vendor A
Database
Vendor B
Database
Tech-Web Client
Version n.n Specification
Vendor A MIMOSA Tech-Web Server
Version n.n Software
Vendor B MIMOSA Tech-Web Client
Version n.n Software
XML Data
Vendor A Supplied
Vendor B Supplied
MIMOSA Production
MIMOSA Beta
Request
MIMOSA Site0 Reference DB Version n.n-yyyy.mm.dd
Technologies
REG (Asset Register Management)
WORK (Work Management)
DIAG (Diagnostics / Recommend.)
TREND (Static Value Trends/Alarms)
DYN (Dynamic Vibration/Sound)
SAMPLE (Oil/Fluid/Gas/Solid Tests)
BLOB (Images/Thermograms/Docs)
REL (Reliability / Data)

## Slide 42: MIMOSA Tech-Web Sample Transaction
Work Request Client
Work Request Server
Client
Database
Database
Interface
XML
Parser
Server
Database
Database
Interface
XML
Parser
Request
Generator
Acknowledge
Generator
HTTP/CGI
HTTP/CGI
HTTP/CGI
Req. Initiation

## Slide 43: MIMOSA OSA-EAI Interfaces
32 Interfaces Production-Ready
  #1110111 TREND-File Import for Service Segments V1.1
  #2110111 TREND-File Import for Assets V1.1
  #1120111 TREND-File Export for Service Segments V1.1
  #2120111 TREND-File Export for Assets V1.1
  #1110111 Dyn-File Import for Service Segments V1.1
  #2110111 Dyn-File Import for Assets V1.1
  #1120111 Dyn-File Export for Service Segments V1.1
  #2120111 Dyn-File Export for Assets V1.1

## Slide 44: MIMOSA OSA-EAI Interfaces
  #1310111 TREND-SQL Client for Service Segments V1.1
  #2310111 TREND-SQL Client for Assets V1.1
  #1320111 TREND-SQL Server for Service Segments V1.1
  #2320111 TREND-SQL Server for Assets V1.1
  #1310111 Dyn-SQL Client for Service Segments V1.1
  #2310111 Dyn-SQL Client for Assets V1.1
  #1320111 Dyn-SQL Server for Service Segments V1.1
  #2320111 Dyn-SQL Server for Assets V1.1

## Slide 45: MIMOSA OSA-EAI Interfaces
  #9610121 Trend-Web Client V2.2
  #9620121 Trend-Web Server V2.2
  #9610221 Dyn-Web Client V2.2
  #9620221 Dyn-Web Server V2.2
  #9610321 Sample-Web Client V2.2
  #9620321 Sample-Web Server V2.2
  #9610421 Blob-Web Client V2.2
  #9620421 Blob-Web Server V2.2
  #9610521 Reg-Web Client V2.2
  #9620521 Reg-Web Server V2.2
  #9610621 Diag-Web Client V2.2
  #9620621 Diag-Web Server V2.2
  #9610721 Rel-Web Client V2.2
  #9620721 Rel-Web Server V2.2
  #9610821 Work-Web Client V2.2
  #9620821 Work-Web Server V2.2

## Slide 46: Planned MIMOSA Technical Development Timeline
Final Version, In Production Use
Development Version, In Beta Use
Draft Version Developed
Notes: This chart shows the planned MIMOSA technical development timeline.

## Slide 47: OSA-EAI Open Specification
MIMOSA OSA-EAI Home Page: www.mimosa.org/osa-eai
Version 2.2 Production Specifications Are Available On the Web At No Cost
Specifications Under Development, Certification Tools, and Other Member-Only Resources Are Available To MIMOSA Members in the MIMOSA Technical Committee Yahoo Group http://groups.yahoo.com/group/mimosatech

## Slide 48
Certified Products Can Be Marked As