## Slide 1: The MIMOSA Architecture Summary
Industry Standard
Vendor Supplied
MIMOSA Production
MIMOSA Beta
MIMOSA Draft
MIMOSA Design Phase
Packaged Technologies [Tech-]
REG (Asset Register Management)
WORK (Work Management)
DIAG (Diagnostics / Health / Rec.) TREND (Static Trends/Alarms)
DYN (Dynamic Vibration/Sound)
SAMPLE (Oil/Fluid/Gas/Solid Tests)
BLOB (Binary Data/Thermography)
REL (Reliability / Data)
Component Condition Monitoring (CM) Layers [Layer-]
DA (Data Acquisition)
DM (Data Manipulation)
SD (State Detection)
HA (Health Assessment)
PA (Prognostic Assessment)
AG (Advisory Generation)
Type I Interfaces
Type II Interfaces
Categories [Category]
Service Segments (“As Designed” Functional Blocks)
Asset (“As Installed” Serialized Physical Objects)
Tech-File
Import
V 2.2
Software
Tech-File
Export
V2.2
Software
Tech-Web
Client
V2.2
Software
Tech-Web
Server
V2.2
Software
Tech-SQL
Client
for Category
V 1.1 Soft.
Tech-SQL
Server
for Category
V 1.1 Soft.
Tech-File
Import
for Category
V 1.1 Soft.
Tech-File
Export
for Category
V 1.1 Soft.
Layer-CM
XML Client V1.0
Software
Layer-CM
XML Server V1.0
Software
Layer-CM
Type Broker
V1.0 Software
Tech-SQL
Client
for Category
V 1.1 Spec.
Tech-SQL
Server
for Category
V 1.1 Spec.
Tech-File
Import
for Category
V 1.1 Spec.
Tech-File
Export
for Category
V 1.1 Spec.
Tech-File
Import
V2.2
Spec.
Tech-File
Export
V2.2
Spec.
Tech-Web
Client
V2.2
Spec. [XSD]
Tech-Web
Server
V2.2
Spec. [XSD]
Layer-CM
XML Client V1.0
Interface Spec.
Layer-CM
XML Server V1.0
Interface Spec.
Layer-CM Type
Broker V1.0
Interface Spec.
ODBC SQL/CLI
Specification
MIMOSA Export
Data (MED) File
Specification
CRIS V1.1
Specification
MIMOSA Site0 Reference
DB V1.1
MIMOSA Site0 Reference DB
V2.2
Common Relational Information Schema V2.2 Specification
MIMOSA Common
XML Message Definition &
CRIS Vocabulary V2.2 Specification
Layer-CM XML
Specification V1.0
[XML Schema]
Layer-CM Object Specification V1.0 [UML]
Layer-CM Interface
Specification V1.0 [IDL]
MIMOSA Object Model (MOM) V1.0
[UML Abstract Type Diagram]
Notes: <number>
<footer>
<header>
<date/time>
This is a complete slide showing the MIMOSA Architecture. Note the Type I interfaces are shown on the left side and the Type II interfaces on the right. The conceptual MIMOSA Object Model (MOM) will “underpin” both CRIS and the Layer-CM Object specifications -- providing the basic Type definitions and relationships which are utilized in CRIS and the Layer-CM object specifications.
The “Layer-CM Type Broker” specification is a specification which allows a supplier to build an compatible interface from a Type II layer interface and through the use of an historical archive function, support a Type I Tech-XML client. The specification will provide guidance to the creation of the broker, but this will be vendor-supplied.

## Slide 2: MIMOSA OSA-EAI V2.2 Interface Concepts
General – All MIMOSA OSA-EAI Interfaces are based on MIMOSA’s Common Relational Information Schema (CRIS). While prior versions of MIMOSA Interfaces have used a variety of enabling technologies, all OSA-EAI V2.2 interfaces will use XML Schema as defined by the W3C.
Tech-File V2.2 Interface Concepts – These interfaces are designed to enable the direct transfer of one entire persistent data store to another one in an industry- standard XML format. They are similar in concept to the earlier Tech-File interfaces, but rather than importing/exporting individual files in a comma delimited format, they enable the transfer of packaged XML documents containing all of the available data. Any given application may include import and/or export capability based on these MIMOSA specifications.
Tech-Web V2.2 Interface Concepts - These interfaces are designed to enable the integration of loosely-coupled Open MRO Applications into Open MRO Solutions in an industry-standard fashion. The interfaces are based on a client/server model and they have been logically organized into Schema Sets or Applications Program Interfaces (APIs) designed to support a series of MIMOSA Technology Types. This allows individual applications that are focused on a specific MRO technology (such as vibration measurement) to integrate with a comprehensive Open MRO Solution by simply supporting the relevant client/server API (in the case of vibration, Dyn).

## Slide 3: MIMOSA Tech-Web V2.2 Interfaces
REG (Asset Register Management) – Enables the integration of Open MRO Applications needing to exchange asset catalog registry information in an industry standard format. The registry includes both asset-specific nameplate information and segment related information. Segment information provides the functional relationship to other segments in a process model while asset information provides the data for the current instance of any asset installed in a given segment. This approach enables life-cycle tracking of MRO data by segment or asset.
WORK (Work Management) – Enables the integration of Open MRO Applications needing to exchange information about request for work and work request along with associated work orders and solution packages that are related to serialized assets or service segments.
DIAG (Diagnostics / Health / Rec.) - Enables retrieval of human or "smart-agent" generated current and/or future proposed asset health states, current and/or future proposed diagnostic failure modes and casual trees, remaining useful life predictions, and recommendations. Also allows access to measurement evidence supporting the diagnoses/prognoses.
  For: Diagnostic Systems
  Prognostic Systems
TREND (Static Trends/Alarms) - Enables retrieval of historical scalar measurements, abnormal data alarms, and operational event logs
  For: Process Data Historians
  Process Condition Monitoring Systems
  Operational Data Systems
DYN (Dynamic Vibration/Sound) - Enables retrieval of historical dynamic measurements (used with vibration and sound monitoring and including frequency spectra measurements and time waveforms), abnormal data alarms, and operational event logs
  For: Vibration Condition Monitoring Systems
  Sound Condition Monitoring Systems

## Slide 4: MIMOSA Tech-Web V2.2 Interfaces (Cont.)
SAMPLE (Oil/Fluid/Gas/Solid Tests) - Enables retrieval of historical fluid, air, and solid sampling data, abnormal data alarms, and operational event logs
  For: Oil Sampling Condition Monitoring Systems
  Air Sampling Condition Monitoring Systems
  Solid Sampling Condition Monitoring Systems
BLOB (Binary Data/Thermography) - Enables retrieval of historical binary large objects (BLOB) measurements (used with thermography and imaging monitoring), abnormal data alarms, and operational event logs
  For: Thermographic Condition Monitoring Systems
  Image Monitoring Systems
REL (Reliability Data)