## Slide 1: Standardising Standards-based Interoperability: The Architecture of the OIIE and OGI Pilot
Matt Selway and Markus Stumptner (Co-CTO MIMOSA)
University of South Australia
June 4, 2019
NIST Open Industrial Digital Ecosystem Summit

## Slide 2
AI and Software Engineering Group
About 20 people
AI + Software Engineering + Data Management
Major topics
  Modelling and reasoning about system behaviour
  Diagnostics, Configuration, Automated Debugging, Natural Language
  Information and knowledge management in distributed ecosystems

## Slide 3
Projects in the Ecosystem Space
OT/IT Interoperability
Digital Information Energy Australia Gateway
OGI Pilot - OIIE
Genetic Data Curation
SOA for Future Combat Systems
Automated Modelling for Combat Simulation Ecosystems
Integrated Law Enforcement – Federated Data Platform

## Slide 4: What is the OIIE?
Open Industrial Interoperability Ecosystem
Framework and architecture for defining and describing standardised and standards-based ways for how systems should interoperate
Aims to support Digitalization, Supplier-neutral, and enable COTS & Open Source Plug ‘n Play Interoperability
Refinement of concepts MIMOSA has been developing for ~15 years
Includes several components:
  Use Case Architecture
  Connectivity and Services Architecture
  Data and Message Models
  Specifications for systems supporting Ecosystem Administration, e.g:
    ws-ISBM, SDAIR, CIR, Services Registry

## Slide 5: Supplier Neutral Industrial Digital Ecosystem Digital Ecosystem Concept Specialized For Process Industries
Enterprise Ecosystem Nodes
Com-ponents
Systems
Network of Enterprise Ecosystems
EPC
Ecosystem
Owner
Operator
Ecosystem
Interoperating Enterprise Digital Ecosystems
Supplier Neutral
Industrial Digital Ecosystem
OEM
Ecosystem
Systems
Com-ponents
Major suppliers of IT Infrastructure and Industrial Applications and Systems all want their ecosystem to be THE Ecosystem.

## Slide 6: What is the OGI Pilot?
Test-bed and proving ground for the OIIE
Where we try to make the OIIE a reality
Previous pilots phases focused on EPCO&M Handover of As-Designed Engineering Data (P&IDs, etc.)
Current pilot phase covers 2 additional major aspects:
  Requests for model information relating to requirements (greenfield) and/or incomplete asset data (brownfield)
  Condition-based Maintenance
Possible areas for future pilot phases:
  Coverage of process design (PFDs)
  Expand Capital Projects Use Cases, full Procurement
  CBO (Condition Based Operations)

## Slide 7
P to B Stack:
Automation ERP
system
Primary business process: Operations
Secondary business process:
Establish and Maintain Operations Capability
Level R4
Level R3
Level R2
Level R0
Level R1
Notes: Briefly mention the focus of the use cases are on the secondary business process.
Focus on areas that will benefit “everyone” without stopping competition in their primary business process.
But can be specialised to other areas and business needs.

## Slide 8: Full Asset Life-cycle Management
Operate & Maintain (O&M)
End of Life
Product Model/Product=Component/Systems(Packages)/System of Systems/Plant/Facility/Platform Life-Cycles
Product
Design
Process
Engineer
Simulate
Completion,
Commission and Startup
Product
MFG
Continuous Improvement Feedback Loops
Construct
Procure
Device/Equip
Manufacturing
Platform Integrator
Capital Project
Owner/Operators
Derived from ISO TC 184
Manufacturing Asset Management Integration Task Force Final Report
Engineer
Design
Notes: Mention ow the use cases cover the asset lifecycle: incremental expansion of the use cases to cover the entire process based on priority/value requirements.

## Slide 9
Capital Projects
Complete/ Commission/ Startup
Operate/ Maintain
Decommission/ Dispose
Sustained Life-cycle Digital Asset Management
OIIE Use Case 1: Information handovers to O&M
OIIE Use Case 2: Recurring Engineering Updates to O & M
OIIE Use Case 3: Field Changes to Plant/Facility engineering
OIIE Use Case 4: Enterprise Product Data Library Management (tied to ISDDs)
OIIE Use Case 5: Asset Installation/Removal Updates
OIIE Use Case 6: Preventive Maintenance Triggering
OIIE Use Case 7: Condition Based Maintenance Triggering
OIIE Use Case 8: Early Warning Notifications
OIIE Use Case 9: Incident Management/Accountability
OIIE Use Case 10: Automated Provisioning of O & M systems
Opportunistic Handover of Structured Digital Assets
Cross Project Activities
OIIE Use Case 11: Enterprise RDL Management
OIIE Use Case 12: RFI and RFI Response (Models Meeting Requirements and Model Information, Green and Brown Field)
OIIE Use Case 13: Lockout/Tagout
Yellow Use Cases in Phase 3.1
OIIE Use Case 14: CBM Data Acquisition
OIIE Use Case 15: Capital Project Asset Install
Standard OIIE/OGI Use Cases

## Slide 10: Components of the OIIE
*Use Case Architecture
Connectivity and Services Architecture
Data and Message Models (CCOM, ISDDs, OAGIS BOD Architecture, etc.)
Specifications for Ecosystem Administration systems

## Slide 11: OIIE/OGI Standardized Use Case Architecture Standardized Methodology to Define and Re-use OIIE Components
Use Cases
Scenarios
(OIIE) Events
Background
Actors
Individual Message Exchange
Scope
Preconditions
Successful End Condition
Data Content
Data Formats
Reference Data
(OIIE) Events
Information Service Bus Configuration
Specific Data Content
Reference implementation using CCOM BODS
Required Data Processing
Expected Response Event
  Actors
  Triggers
  Process Workflows
  Scenarios
User Stories
High-level
Pictographic
Depict 1 or more Use Cases, Scenarios, and/or Events
Actors, Systems, Exchanges, Data
User Stories

## Slide 12: Definitions in Brief
Use Case
  general description of interactions to achieve an interoperability goal within a specified scope and background context
Scenario
  specific description of a group of events that achieve an interaction detailing data and configuration requirements; multiple scenarios may be required to achieve the goal of a use case and the same scenario may be reused by multiple use cases

## Slide 13: Definitions in Brief
Event
  individual message exchange between systems detailing data and processing requirements
User Story
  high-level graphical representation of interactions and events defined by one or more use cases and/or scenarios

## Slide 14: UC-5: Asset Installation/Removal Updates (Abridged)
Overview This Use Case describes the process for updating O&M systems of serialized asset configuration updates. The updates originate from a Work Management System (WMS) and may include verification against sensed install/removes originating from an Intelligent Automation Bus (IAB).
Background
One of the largest headaches for any complex facility or plant is keeping accurate track if serialized assets currently installed in a given functional location. Experience has shown that substantial process and information gaps routinely exist and there are often substantial gaps after a few years of operating.
Notes: Go through these briefly. Want them here for people to reference in the slide deck later.

## Slide 15: UC-5: Asset Installation/Removal Updates (Abridged)
Scope The scope of this Use Case is limited to remove and replace corrective maintenance.
[NOTE: The reuse aspects of the Use Case Architecture mean that the Scenarios and Events (and their implementations) are reused in other Use Cases, such as Capital Project Asset Installation]
Preconditions
Information Handover to O&M and O&M Provisioning must have occurred prior to this Use Case so that the WMS, IAB, and other O&M systems are populated with functional location and asset information.

## Slide 16: UC-5: Asset Installation/Removal Updates (Abridged)
Successful End Condition A reconciled, completed work order for asset removal/installation has been published to any interested O&M systems.
Actors
Business Actors:
Operations; Maintenance Planner; Technician
System Actors:
Maintenance/Work Management System; I&C Device Monitoring System (IAB)

## Slide 17: UC-5: Asset Installation/Removal Updates (Abridged)
Triggers Operations sends a work request to Maintenance identifying a particular plant item that needs maintenance.
Main Success Scenario
(see next slide)
Send work request | Operations sends a work request to Maintenance identifying a particular plant item that needs maintenance.
Generate and approve work order and schedule | The Maintenance Planner generates a work order and schedule in the Maintenance Management System against a functional location or asset. The work order is given approval by Operations.
… | …

## Slide 18: UC-5: Asset Installation/Removal Updates Example Workflow

## Slide 19: UC-5: Asset Installation/Removal Updates (Abridged)
System Interoperability Scenarios
Scenario 10 – Push Intelligent Device Removal/Installation Events from CMS to MMS
Scenario 11 – Publish Asset Removal/Installation Events from MMS to O&M
Version Applicability/Alignment
[indicates with which version of CCOM and/or other specifications the Use Case is compatible]
Document Versioning
[Table of major revisions, dates, and the major changes.]

## Slide 20: SC-10: Push Intelligent Device Removal/Installation Events from CMS to MMS (Abridged)
Overview
This Scenario details an Intelligent Automation Bus system sensing an asset removal/installation at a functional location and notifying another OIIE enabled system, such as a Work Management System being used for maintenance work orders.
[Note: Here ‘event(s)’ refers to the AssetSegmentEvent element of CCOM]
Actors
[system actors only in Scenarios]
IAB System | Notify OIIE Systems of changes in asset configuration
Work Management System | Receive notifications from IAB System of changes in asset configuration. Associate asset removal/installation with work order.

## Slide 21: SC-10: Push Intelligent Device Removal/Installation Events from CMS to MMS (Abridged)
Data Content
The data sent from the IAB to the WMS is at least:
Functional location; serialized asset; timestamp when install/remove occurred
Additional contextual data may be sent:
Agent performing the work; calendared maintenance work order
MIMOSA CCOM Reference Types
[lists general types and relevant specific reference data that is to be used]
‘Installation of Asset on Segment’ EventType, UUID: ecc99353-412b-4995-bd71-1cbc6fc16c7c
‘Removal of Asset on Segment’ Event Type, UUID: 3a45e126-b234-42a0-b3b1-07c29522d02d

## Slide 22: SC-10: Push Intelligent Device Removal/Installation Events from CMS to MMS (Abridged)
Data Formats
[Indicates any constraints on specific data formats]
The data published by the IAB System and received by the Work Management System must conform to MIMOSA CCOM BODs.
[Note: Does not specify which BODs; the Events determine that.]
System Interoperability Events
Push Asset Segment Event Data
  This maps to a request-response BOD pair: ProcessAssetSegmentEvents, AcknowledgeAssetSegmentEvents
[there may be several events, but only 1 in this Scenario]

## Slide 23: SC-10: Push Intelligent Device Removal/Installation Events from CMS to MMS (Abridged)
Infrastructural Components
[includes requirements based around the use of specific OIIE components such as the ISBM, SDAIR, Transform Engine, CIR, etc.]
ISBM
The communication between all systems occurs via the ISBM using request-response services.
Implementation Requirements
The IAB System must implement a client for the Consumer Request and Channel Management (GetChannel operation only) Services
The Work Management System must implement a client for the Provider Request and Channel Management (GetChannel operation only) Services
Both systems may implement a client for the Notification Services

## Slide 24: SC-10: Push Intelligent Device Removal/Installation Events from CMS to MMS (Abridged)
Suggested Channel/Topic Configuration
Channels and topics should be declared following the ISBM Guidelines.
Example channel path:
/Enterprise/Refinery A/Area A/Light Ends Area/ISO18435:D1.3
Example Topic Name:
OIIE:S10:V1.1/CCOM-XML:ProcessAssetSegmentEvents:V1.0
Event Sequence
(see next slide)

## Slide 25: SC-10: Push Intelligent Device Removal/Installation Events from CMS to MMS Event Sequence

## Slide 26: SC-11: Publish Asset Removal/Installation events from MMS to O&M (Abridged)
Overview
In order to notify other O&M systems that a serialized asset has been installed or removed, the Work Management System (WMS) publishes an asset install or removal event to all relevant O&M systems.
Actors
[system actors only in Scenarios]
Work Management System | Send notifications of changes in asset configuration
O&M Systems | Receive notifications of changes in asset configuration

## Slide 27: SC-11: Publish Asset Removal/Installation events from MMS to O&M (Abridged)
Data Content
The data sent from the WMS to other O&M Systems is at least:
Functional location; serialized asset; timestamp when install/remove occurred
Additional contextual data may be sent:
Agent performing the work; calendared maintenance work order
MIMOSA CCOM Reference Types
‘Installation of Asset on Segment’ EventType, UUID: ecc99353-412b-4995-bd71-1cbc6fc16c7c
‘Removal of Asset on Segment’ Event Type, UUID: 3a45e126-b234-42a0-b3b1-07c29522d02d

## Slide 28: SC-11: Publish Asset Removal/Installation events from MMS to O&M (Abridged)
Data Formats
[Indicates any constraints on specific data formats]
The data published by the Work Management System and received by other O&M Systems must conform to MIMOSA CCOM BODs.
[Note: Does not specify which BODs; the Events determine that.]
System Interoperability Events
Publish Asset Segment Event Data
  This maps to a publish-subscribe BOD: SyncAssetSegmentEvents

## Slide 29: SC-11: Publish Asset Removal/Installation events from MMS to O&M (Abridged)
Infrastructural Components
ISBM
The communication between all systems occurs via the ISBM using publish-subscribe services.
Implementation Requirements
The Work Management System must implement a client for the Provider Publication and Channel Management (only the GetChannel operation) Services.
O&M Systems must implement a client for the Consumer Publication and Channel Management (only the GetChannel operation) Services. O&M Systems may implement the ISBM Notify Listener Service for message notification.

## Slide 30: SC-11: Publish Asset Removal/Installation events from MMS to O&M (Abridged)
Suggested Channel/Topic Configuration
Channels and topics should be declared following the ISBM Guidelines.
Example channel path:
/Enterprise/Refinery A/Area A/Light Ends Area/ISO18435:D1.3
Example Topic Name:
OIIE:S11:V1.1/CCOM-XML:SyncAssetSegmentEvents:V1.0
Event Sequence
(see next slide)

## Slide 31: SC-11: Publish Asset Removal/Installation events from MMS to O&M Event Sequence

## Slide 32: Story M100: Start Unit Functional Requirements
Client Business Person
1.We need to build a light ends unit to remove butane from our incoming crude supply
Client Engineer
2.a How Much Capacity Do We Need?
b. What will the incoming crude spec be?
Debutanizer
PFD and P&ID
Functional Requirements
A

## Slide 33: Story M101: Model Selection
Client Engineering Person
1. We need to buy equipment and instruments meeting or exceeding functional requirements taken from PFD and P&IDs for the new Debutanizer Tower.
Client
Purchasing
2. Send me the Requirements from those documents and I will check with our preferred suppliers.
Debutanizer
PFD and P&ID
Instrument or Equipment Supplier Portals
Requirements (RFI)
Models Meeting Requirements (RFI Response)
Requirements
A
B
3.P2M Dialog

## Slide 34: Components of the OIIE
Use Case Architecture
*Connectivity and Services Architecture
Specifications for Ecosystem Administration systems
Data and Message Models (CCOM, ISDDs, OAGIS BOD Architecture, etc.)

## Slide 35
Manufacturers
IT Networks
Automation and Control
Enterprise Business Systems
EPC Firms
IT Networks
Engineering , Procurement and Construction
Owner/Operators
IT Networks
Automation and Control
Enterprise Business Systems
Manufactured Asset Data
(Make/Model Information, Serial #)
Operations & Maintenance Data
(Monitoring, Diagnostics Prognostics)
PFD, P&ID, Tags, Docs
& Requirements
OEMs
Functional and Technical Requirements
Business Requirements
Model and Instance Information
OIIE Inter-Enterprise Systems Connectivity and Services Architecture
Enabling Industry 4.0
Notes: 7ohnyMy liukmhmmmm

## Slide 36: OIIE Intra-Enterprise Systems Connectivity and Services Architecture
Enterprise Business Systems
Engineering Design
IEC 62264 Messaging Service Model /OpenO&M Information Service Bus Model
Construction Management
Automation and Control
HSE and Operation Monitoring
Prognostic & Health Management
Automation Control Bus
Device
Sensor/ Transducer
Planning
Operations Management
Operations Risk Management
Maintenance Management
Trusted
Systems
Enterprise Reference Data Libraries
IIoT Device Metadata
OIIE Administration
Device
IIOT Device
Standard, Cloud Friendly Enterprise Solutions Architecture For Digital Business Ecosystems
IIoT Connections
ISBM Web Services
Industry Reference Data Libraries
IIoT Device Metadata
(ISO 15926, OTD, CDD…)
Shared Information and Semantic Context
(Constrained)
(Constrained)
Connectivity Legend
Inter-Enterprise Connections
Trusted IT/OT connections

## Slide 37: Components of the OIIE
Use Case Architecture
Connectivity and Services Architecture
*Specifications for Ecosystem Administration systems
Data and Message Models (CCOM, ISDDs, OAGIS BOD Architecture, etc.)

## Slide 38: OpenO&M ws-ISBM
Backbone of the OIIE Architecture
Web Service definitions (SOAP) for Enterprise Service Buses supporting request-response and publish-subscribe messaging modalities plus push notifications
Interactions defined through web-services:
  Channel Management Service: channel, security configuration
  Notification Service: allow notifications of new messages
  Provider Publication Service: publish messages
  Consumer Publication Service: read published messages
  Provider Request Service: read and respond to requests
  Consumer Request Service: send requests and read responses

## Slide 39: Typical Publish-Subscribe Interaction
Consumer
Provider
ISBM instance
Consumer
OpenSubscriptionSession Parameters: Channel, Topic, …
OpenPublicationSession Parameters: Channel, …
PostPublication Parameters: Topic(s), Message, …
NotifyListener Parameters: Session, Topic(s), …
ReadPublication Parameters: Session
Message Content
ExpirePublication
Parameters: Session, MessageID

## Slide 40: Typical Publish-Subscribe Interaction
Provider
ISBM instance
Consumer
RemovePublication Parameters: Session
ClosePublicationSession Parameters: Session
CloseSubscriptionSession Parameters: Session

## Slide 41: Typical Request-Response Interaction
Consumer
ISBM instance
Provider
OpenProviderSession Parameters: Channel, Topic(s), …
OpenConsumerSession Parameters: Channel, ListenerURL
PostRequest Parameters: Topic, Message, …
NotifyListener Parameters: Session, Topic(s), …
ReadRequest Parameters: Session
Message Content
ExpireRequest
Parameters: Session, MessageID
Processing

## Slide 42: Typical Request-Response Interaction
Consumer
ISBM instance
Provider
RemoveRequest Parameters: Session
ReadResponse Parameters: Session
CloseSubscriptionSession Parameters: Session
PostResponse Parameters: RequestID, Message, …
CloseConsumerSession Parameters: Session
NotifyListener Parameters: Session, Topic(s), …
Message Content

## Slide 43: OpenO&M ws-ISBM v1.1
Currently updating the specification to version 1.1
Major addition is a new RESTful interface with JSON support
Improvements and generalisations to support mixed content and transparency between the SOAP/XML interface and a REST/JSON interface
Clarification of security elements and their management
Version 1.1 is being validated as part of the OGI Pilot

## Slide 44: SDAIR: Structured Digital Asset Interoperability Register
Provides several functions for an OIIE:
  Various aspects of OIIE Configuration
  Register and mapping of (multiple) Tag Identifiers to UUIDs to facilitate CCOM-based exchanges
  Managing primary enterprise breakdown structure and associated OIIE configuration: cross-domain
  Managing ISDDs and their mappings
  Register of assets, functional locations, breakdown structures, etc., as required to achieve OIIE functionality, particularly for cross-domain data that no individual system can typically maintain
Functional definition only: vendors can provide various implementations as long as they fulfil the requirements and conform to the OIIE interfaces

## Slide 45: OpenO&M CIR: Common Interoperability Register
Provides mapping services between identifiers of different systems
In contrast to SDAIR which provides more “internal” mappings, SDAIR provides more “external” mappings
General example usage is to resolve against common reference data before exchanging a message, e.g.:
  System A queries CIR for IDs according to specific reference data library
  CIR responds with IDs matching the query
  System A sends message to System B using CIR provided IDs
  System B receives message and queries CIR for IDs related to its own systems
  CIR responds with IDs matching the query
  System B can then process its data in its own way

## Slide 46: Services Register
The Services Register supports the configuration and discoverability of systems and services in the OIIE
Description of channel/topic configurations
For example, consumers can query it for services publishing information of interest and then subscribe to those channels/topics
Not used in the current Pilot but ultimately an integral part of the ecosystem administration

## Slide 47: Components of the OIIE
Use Case Architecture
Connectivity and Services Architecture
Specifications for Ecosystem Administration systems
*Data and Message Models (CCOM, ISDDs, OAGIS BOD Architecture, etc.)

## Slide 48: Message and Content Models
Bring standards together that provide value and meet requirements:
  MIMOSA CCOM—Asset Lifecycle Modelling
  ISDDs (Industry Standard Datasheet Definitions)—Datasheet models for functional locations, models, and assets, based on:
    API, ASME, IEC, ISA, ISO, NORSOK and PIP
  OAGIS BOD Architecture—Message Model
  ISO 13374—Condition Based Maintenance (incorporated into CCOM)
  Reference Data from various sources: ISO 15926, ISA, ISO 14224, …
Placeholders for other standards at different levels, but currently focused on those above

## Slide 49: Contextualization for Open Industrial Interoperability Ecosystem using MIMOSA CCOM 4.x, ISA, OAGi, ISO and IEC Standards
Process Engineering-(CCOM Segment Networks)- Process Flow Diagrams
  Work Processes followed for CAPEX and OPEX (Intra and Inter-Enterprise)
  Production Process to be supported by Plant/Platform/Facility
Functional/Systems Engineering-(CCOM Segment Networks)- P&IDs, other schema
  System of Systems
  Systems (Functional Packages)
  Functional Locations (P&ID Tag)
  Components
  Sensors
Models - (CCOM Model) – Used for MFG Model and Package Model
Serialized Equipment & Devices-(CCOM Assets installed in CCOM Functional Locations)
Multiple Breakdown Structures as Needed- Taxonomic views of same CCOM objects
  Enterprise Breakdown – Enterprise/Area/Unit (ISA 95/88)
  Maintenance Breakdown Structure - (e.g. ISO 14224)
ISDDs - Property Sets for ALL Functional Locations, Equipment and Devices
IIOT- Data captured by Sensors is Contextualized by ALL of Above

## Slide 50: Business Object Documents (BODs)
MIMOSA adopted OAGIS Business Object Document Architecture for structuring messages and defining the behaviour of encapsulated MIMOSA CCOM payloads
Allows consistent structure and metadata regardless of data format or protocol
Each BOD schema specifies criteria on message content  used to implement OIIE Events
Supported Verbs
  Get, Show, Sync, Process, Acknowledge, Confirm
  Get/Show, Process/Acknowledge  Request-Response
  Sync  Publish-Subscribe
Application Area
Data Area
Verb
Noun
MIMOSA CCOM Payload
Business Object Document

## Slide 51: CCOM BODs Conceptual Approach Example
*Request For Information
Respond By = 2018-06-06
Request Type
Model Request for Asset
Asset
Serial No. = XYZ0001
Attribute Set
Attribute Group
Attribute
Model Spec. No. = …
Attribute Group
Attribute
Temp. Min. = -15o
Segment
Functional Location TS001
Attribute Set
ISDD Instance
Attribute
Temp. Max. = 90o
Agent
Owner/Operator
Asset Installation Event
Installed At: 2017-06-06
BOD Noun
Process Model Request For Asset
from
about
installed asset
installed location
type
has
has
has
has
has
has
Model Request (Request For Information)
From Agent (Agent: Owner/Operator)
Asset (Asset: with S/N XYZ0001)
From Agent (Agent: Owner/Operator)
Serial Number (XYZ0001)
Functional Location (Segment: Functional Location TS001)
Asset Installation Date (2017-06-06)
Functional Requirements (Attribute Set: ISDD Instance)
Group (Attribute Group)
Attribute (Attribute: Temp. Min. = -15o)
Attribute (Attribute: Temp. Max. = 90o)
Respond By (2018-06-06)
Notes: * Indicates object of interest
A standard CCOM XML dump of the left-hand side would result in a deeply nested structure containing everything on the left.
For a BOD, the depth is restricted and important information explicitly represented at the top-level of the “noun”, even if it is far away from the main object of interest (i.e. the Request for Information object)
If the first degree of separation is always nested for the primary object of interest, there may be some duplication of references. (e.g. ‘From Agent’)
This nested information can be left out as it can be reconstructed from the BOD contents.

## Slide 52: Industry Standard Datasheet Definitions (ISDDs)
Capture existing Industry Standard Datasheets as machine interpretable business objects to make them fully re-usable, mappable, and extensible.
  Provide standard (XML) exchange schema for exchanging datasheet-oriented information
  Mappable to existing OEM and O/O Datasheets
Capture high-value properties from existing data sheets published by credible industry associations, such as:
  API, ASME, IEC, ISA, ISO, NORSOK and PIP.
Support Asset’s full life-cycle information management
  Data sheets are not used just for procurement
  Improves ability to procure, install, commission, operate and maintain assets with reduced effort, cost and schedule

## Slide 53: Types of Data Sheet
Functional Segments can be associated with data sheets to specify functional requirements
Models can be associated with data sheets to specify characteristics of equipment of that model
Equipment Assets can be associated with data sheets to specify characteristics of that equipment
Segment and Asset Types can have data sheet templates to support class libraries

## Slide 54: ISDD Example
Equipment Type
Temperature Transmitter
Property Set Definition
20T2221 Device Specifications
Property Group Definition
RESPONSIBLE ORGANIZATIONS
Property Definition
Housing Type (Line 12)
Property Type
Housing Type
Enumeration
Housing Type
Enumeration Items
Extruder bolt
High pressure
Property Group Definition
PROTECTIVE SHEATH AND FITTING
Property Set Definition
20T1001 Operating Parameters
Property Definition
Pad/Collar Type (Line 13)
Property Type
Pad/Collar Type
ISA 20T2221 Datasheet
ISA 20T2221 Picklist

## Slide 55: ISDD Example Instance
Equipment Type
Temperature Transmitter
Property Set
20T2221 Device Specifications
Property Group
RESPONSIBLE ORGANIZATIONS
Property
Housing Type = high pressure
Property Group
PROTECTIVE SHEATH AND FITTING
Property Set
20T1001 Operating Parameters
Property
Pad/Collar Type = 1x1 flat parallel
ISA 20T2221 Datasheet
ISA 20T2221 Picklist
Attribute Type
Housing Type
Enumeration
Housing Type
Enumeration Items
Extruder bolt
High pressure
Property
Fitting conn nominal size = ½ in
Property
Mounting fitting type = compression
….

## Slide 56: How to connect to the OIIE?

## Slide 57: OIIE Adaptors
Each system/application participating in OIIE exchanges must have an adaptor
Can be considered in two parts:
  CCOM (or data) adaptor: converts internal data format to MIMOSA CCOM
  ISBM adaptor: communication with ISBM

## Slide 58: Building an OIIE Adaptor (Simplified)
Obtain Web-service definitions
  SOAP/XML-based using WSDL
  REST/JSON-based using OpenAPI
Determine in which OIIE Use Case(s), Scenario(s), and Event(s) the application will participate
Identify the CCOM data elements and BODs must be supported
Map internal data to CCOM data elements
Identify the ISBM services to be implemented
Implement required services, mappings, and other considerations (e.g., error logging, auditing, persistence, UIs, etc.)

## Slide 59: OGI Pilot CBM Demo

## Slide 60: OIIE OGI Pilot Phase 3.1 Activities 1-4 (end 2018 – mid-2019)
Debutanizer Tower Condenser Unit P&ID
Worley Parsons: Hexagon (Proteus XML)
P&ID Logical Connection information
MIMOSA Structured Digital Asset Interoperability Registry
RFI/RFI Response (Greenfield)
RFI Response – Models
RFI – Functional requirements
Capital Project Asset Installation
Request for Model properties (ISDDs)
Asset instances selected from RFI Response (defined using ISDDs)
Installed on P&ID Tag locations (defined using ISDDs)
EPC
OEM
Procure
w/ OAGIS
Use Cases ISDD Based Way of Specifying, Selecting and Buying Devices and Equipment
Use Case Adding As-Built Information Using OIIE Events
Adding Detail to Prior Work
As-Designed O&M Takeoff using CCOM or Proteus

## Slide 61: OIIE OGI Pilot Phase 3.1 Activities 5-8 (end 2018 – mid-2019)
Information Handover
From Capital Project to Operations and Maintenance
Condition Based Maintenance
Remove and Replace
Diagnostics
RFI/RFI Response
(Brownfield) Information Remediation
Over ISBM (Information Service Bus Model)
Prognostics
Advisory Generation

## Slide 62: Questions?

## Slide 63: OIIE Systems and Scenarios Landscape
SDAIR

## Slide 64: CBM According to ISO 13374
ADVISORY GENERATION (AG)
PROGNOSTICS ASSESSMENT (PA)
HEALTH ASSESSMENT (HA)
STATE DETECTION (SD)
DATA MANIPULATION (DM)
DATA ACQUISITION (DA)
External Systems,
Data Archiving, & Block Configuration
Technical Displays & Information Presentation
Machine condition assessment data processing & information flow blocks.
Sensor / Transducer / Manual Entry

## Slide 65: Condition Based Maintenance and IIoT
Inter-Enterprise via ISBM
Automated System Bus
Operational Risk Management System
Device Manufacturer Supplying Remote Diagnostic/Prognostic/Advisory Support
Owner/Operator
Intra-Enterprise ISBM
IIoT Device
IIoT Device
Automation and Control
HSE and Operation Monitoring
Prognostic & Health Management
Sensor/ Transducer
Device
Device
HSE and Operation Monitoring
Prognostic & Health Management
Maintenance Management System
IIoT Device
May be same physical instance as the intra-enterprise ISBM
Internally may have some or none of these systems.
Support for different protocols as required by industry.
Support for different protocols as required by industry.
Supports remote queries for measurement data and publishes advisories via ISBM.
SDAIR
Registry of digital asset data for contextualisation.
ERP
Notes: Architectural diagram
Sensors -> Measurements -> Diagnostics/Prognostics (Analysis) -> Advisory (Operational Risk Management System) -> Maintenance Management System
Diagnostics/Prognostics may come from same “chip”
Local diagnostic/advisory (Control System and/or ISBM)
Inter-enterprise diagnostic/measurement info: query-based over ISBM
Show both OPC UA and CCOM REST/JSON API

## Slide 66: CCOM Contextualisation—Maintained by SDAIR
Measurement
Recorded at: 2018-06-01:01:00
Measurement
Recorded at: 2018-06-01:01:00
Asset
Debutanizer
Serial # DZR-3246
Model
Debutanizer DZR 5000
Breakdown Structure
Primary
Segment
Debutanizer Tower T100
Segment
Debutanizer Feed
Segment
Condenser C200
Segment
Temperature Sensor TS-1
Asset
Tower
Serial # T-456
Asset
Pipe Section
Asset
Condenser
Serial # CF332
Asset
Temp. Sensor
Serial # TS-999
AssetSegmentEvent
Install
1 Jan 2018
AssetSegmentEvent
Install 1 Jan 2018
AssetSegmentEvent
Install 1 Jan 2018
AssetSegmentEvent
Install 1 Jan 2018
Supports both Asset-
and Segment-based
MeasurementLocations
Transducer
Segment
Temperature Sensor TS-2
AttributeSet
Custom Measurement Data
Measurement
Recorded at: 2018-06-01:01:00
Measurement
10oC at: 2018-06-01:01:00
Measurement
Recorded at: 2018-06-01:01:00
Measurement
Recorded at: 2018-06-01:01:00
Measurement
Recorded at: 2018-06-01:01:00
Measurement
4oC at: 2018-06-01:01:00
Measurement Location
Temp. Loc. 2
Measurement Location
Temp. Loc. 1
Each object uniquely identified by a UUID. Also refer back to the system of record.

## Slide 67: CCOM Contextualisation—Configuration Change Remove/Replace
Measurement
Recorded at: 2018-06-01:01:00
Measurement
Recorded at: 2018-06-01:01:00
Asset
Debutanizer
Serial # DZR-3246
Model
Debutanizer DZR 5000
Breakdown Structure
Primary
Segment
Debutanizer Tower T100
Segment
Debutanizer Feed
Segment
Condenser C200
Segment
Temperature Sensor TS-1
Asset
Tower
Serial # T-456
Asset
Pipe Section
Asset
Condenser
Serial # CF332
Asset
Temp. Sensor
Serial # TS-999
AssetSegmentEvent
Install
1 Jan 2018
AssetSegmentEvent
Install 1 Jan 2018
AssetSegmentEvent
Install 1 Jan 2018
AssetSegmentEvent
Install 1 Jan 2018
Supports both Asset-
and Segment-based
MeasurementLocations
Transducer
Segment
Temperature Sensor TS-2
AttributeSet
Custom Measurement Data
Measurement
Recorded at: 2018-06-01:01:00
Measurement
10oC at: 2018-06-01:01:00
Measurement
Recorded at: 2018-06-01:01:00
Measurement
Recorded at: 2018-06-01:01:00
Measurement
Recorded at: 2018-06-01:01:00
Measurement
4oC at: 2018-06-01:01:00
Measurement Location
Temp. Loc. 2
Measurement Location
Temp. Loc. 1
AssetSegmentEvent
Remove 2 Jan 2018
Asset
Pipe Section
AssetSegmentEvent
Install 3 Jan 2018

## Slide 68: Example—Mesh Networks
Model
Debutanizer DZR 5000
Segment Mesh
DZR Connections
Segment
Debutanizer Feed
Segment
Debutanizer Tower T100
Segment
Overhead Piping Segment
Segment Connection
Segment Connection
Segment
Feed Outlet
Segment
T100 Inlet
Segment
Debutanizer Overhead Inlet
Segment
T100 Outlet A
parent
parent
parent
parent
from
to
from
to
And similar at
the Asset level
Segment Connection
.
.
.
Segment
…
Segment
… Inlet
Segment
… Outlet
parent
parent
from
to
Segment
…